## Slide 1
Sheffield Hackspace
Arduino Day 2015

## Slide 2
Writing An Arduino Sketch
In the previous presentation we used a sketch called “blink” to test the IDE and Arduino board were talking to each other. In this guide we will walk through the process of writing your own sketch to flash the LED attached to pin 13 on your Arduino board.
We will discuss the structure of a sketch, the syntax and the keywords, or functions, that make the program do what you want

## Slide 3
Writing An Arduino Sketch
In order to function correctly an Arduino sketch must have a minimum of two blocks of code, one called “setup” and the other called “loop”
The “setup” function will only run once and will contain code that will setup you board, for example you can tell it which pins are connected to inputs (switches, sensors, etc) and which are outputs (LEDs, motors, buzzers, etc).
The “loop” function contains the main code and runs in a continuous loop.

## Slide 4
Writing An Arduino Sketch
We will write the setup function first. To start you must first declare the function by typing …
void setup() {
}
The “void” part simply states the output of the function, this only become relevant when writing more complex code so can be ignored for now. The code we want to run is entered between the curly braces

## Slide 5
Writing An Arduino Sketch
As this is a simple sketch we only need to put one line in the setup code, and that is to tell the Arduino that pin 13 is being used as an output. We do this by using the keyword “pinMode”
Using this syntax as an example if we wanted to connect a button to pin 5 we would write
pinMode(5, INPUT);
The “;” at the end of the statement simply lets the IDE know that you are done writing
void setup() {
}
pinMode(13, OUTPUT);

## Slide 6
Writing An Arduino Sketch
Next we need to declare our loop function. We do this in exactly the same way we did our setup function earlier
Again the code we want to run all be contained with the curly braces
void setup() {
pinMode(13, OUTPUT);
}
void loop() {
}

## Slide 7
Writing An Arduino Sketch
The purpose of this sketch is to turn an LED on and off continuously. To do this we need to use two different keywords, like pinMode() from earlier.
The first of these is digitalWrite(). In exactly the same way the pinMode() had some extra parameters in the brackets after it we need to do the same for digitalWrite(). The extra parameters are the number of the pin you want to change the state of, and whether you want it on or off (or high or low).
For our purposes we want to turn pin 13 on so we need to write
pinMode(13, HIGH);

## Slide 8
Writing An Arduino Sketch
The next function we need to use is called delay(). As the name would suggest this function causes the Arduino to pause for a set amount of time, in milliseconds. The length of the pause is written in the brackets.
The blink sketch we have already uploaded to the board had a 1 second (1000 millisecond) delay so lets use half a second for our sketch so we can tell it has been uploaded successfully.
delay(500);

## Slide 9
Writing An Arduino Sketch
Our code should now look something like this…
When the Arduino gets to the end of the loop code it returns to the first line and starts again so as it stands when our LED has turned on the code will repeat and turn it on again, without turning it off in-between. How do we solve this?
void setup() {
pinMode(13, OUTPUT);
}
void loop() {
}
digitalWrite(13, HIGH);
delay(500);

## Slide 10
Writing An Arduino Sketch
By copying and pasting the existing loop code, and changing the digitalWrite from HIGH to LOW we should have a sketch that does exactly what we want
void setup() {
pinMode(13, OUTPUT);
}
void loop() {
digitalWrite(13, HIGH);
delay(500);
}
digitalWrite(13, LOW);
delay(500);
Lets upload it to the Arduino and find out…

## Slide 11
Writing An Arduino Sketch
Congratulations you’ve just written your first sketch for Arduino! How could you change it? Make it faster or slower? Have the LED on for longer than it’s off? Make it flash a morse code S.O.S?
The last thing we will consider is comments. Adding comments to your code can be extremely useful for keeping track of what each line of code does. If you add // at the end of a line of text the IDE will know it is not code and will ignore it until the next line. If you add a /* the IDE will ignore everything until you add a */ - Our code would look like this

## Slide 12
Writing An Arduino Sketch
/*
My very first Arduino Sketch
Written on Arduino Day 2015 - 28/03/2015
*/
void setup() { // insert setup code inside these brackets
pinMode(13, OUTPUT); // tells Arduino that pin 13 is an output
}
void loop() { // insert loop code inside these brackets
digitalWrite(13, HIGH); // turns the LED on pin 13 on
delay(500); // sets a pause of half a second
digitalWrite(13, LOW); // turns the LED on pin 13 off
delay(500); // sets a pause of half a second
}